## Slide 1
Abaqus training
Keng-Wit Lim
Senior Staff II
Date

## Slide 2: Abaqus Training Materials
Elementary tutorials on GitHub:
https://github.com/kengwitSGH/AbaqusTraining
  Currently, we have 5 tutorials. Will develop more as time goes.
Intermediate (this presentation)
Advanced (in development)
Will find way to migrate to SGH internal server (GitLab)

## Slide 3: Elementary Tutorials on GitHub
Folders containing tutorial and associated input files

## Slide 4: Elementary Tutorials on GitHub (cont’d)
General information
Lesson content

## Slide 5: Elementary Tutorials on GitHub (cont’d)
Small examples (single to a few elements) to test features commonly used at SGH

## Slide 6: Elementary Tutorials on GitHub (cont’d)
Exercises
Additional notes
Links to comments (on Milo)

## Slide 7: Elementary Tutorials on GitHub (cont’d)
Exercises
Additional notes
Links to comments (on Milo)

## Slide 8: Goal of This Training
This training – perform single element tests to test material response under triaxial stress states.

## Slide 9: Performing elemental tests
Why is performing elemental tests important?
  Gives insight into material response
  See main features of material model
  See how parameters affect response
  See limitations of material model (VERY IMPORTANT)
  Helps with interpretation of test data
  Provides a common framework to discuss material response (as opposed to making weak analogies to “non-linear spring”, which is grossly incorrect)

## Slide 10: Triaxial stress state
Common test used for probing stress-strain response:
  Metals – uniaxial compression, uniaxial tension
  Soil – confined triaxial extension/compression
  Concrete – uniaxial compression, uniaxial tension
Not the only stress-state possible.

## Slide 11: Triaxial stress state (cont’d)
Vertical stress
Lateral stress (constant; zero for uniaxial tests)
Shear stress (stress difference)
Pressure (mean stress)

## Slide 12: Commonly Used Material Models at SGH
Commonly used models:
  Metal plasticity
  Concrete
  Soil, granular media (Mohr-Coulomb)
Rate-independent model
Elastic-plastic materials
Quasi-static applications and monotonic loading (models are derived from tests)
For dynamics, ask others.

## Slide 13: Metal Plasticity

## Slide 14: Metal Plasticity
Yield function
Isotropic hardening

## Slide 15: Mohr-Coulomb

## Slide 16: Mohr-Coulomb
Yield function
Isotropic hardening

## Slide 17: Concrete

## Slide 18: Concrete
Yield function
Isotropic hardening